## Slide 1: Vision Pipeline
ARDUINO · TRANSPARENT OLED · COMPUTER VISION
Teaching a transparent OLED to point toward — and resize itself for — a water bottle, using two open vision models feeding one Arduino Uno.
YOLOv8n
Depth Anything V2
Arduino Uno

## Slide 2: What this demo does
01
Watch
A Logitech webcam watches for a water bottle in frame.
02
Locate
YOLOv8n finds it and works out left, right, or centered — the OLED draws a matching arrow.
03
Gauge distance
Depth Anything V2 estimates how near or far the bottle is — the arrow grows or shrinks to match.

## Slide 3: The pipeline
01
Webcam
Live frame from the Logitech C615
02
YOLOv8n
Detects the bottle, picks left / right / center
03
Depth Anything
Estimates distance on the bottle's own crop
04
Serial link
Two bytes: direction + size tier, 115200 baud
05
Arduino + OLED
Draws the arrow, scaled to size
Stages 01–03 run on the PC. Stages 04–05 run on the Arduino Uno.

## Slide 4: YOLO
MODEL 01 · DETECTION
You Only Look Once
YEAR
2015 paper · 2016 at CVPR
INVENTORS
Joseph Redmon, Santosh Divvala, Ross Girshick, Ali Farhadi
ORIGIN
University of Washington
IN THIS PROJECT
YOLOv8n, by Ultralytics (2023) — pretrained on COCO, restricted to class 39: "bottle"
YOLO reframed detection as a single regression pass over the image, predicting every box and class at once — the breakthrough that made real-time detection practical.

## Slide 5: Depth Anything
MODEL 02 · DEPTH
Monocular depth estimation from large-scale unlabeled data
YEAR
2024 (V1 & V2)
INVENTORS
Lihe Yang, Bingyi Kang, Zilong Huang, Xiaogang Xu, Jiashi Feng, Hengshuang Zhao
ORIGIN
The University of Hong Kong & TikTok
IN THIS PROJECT
Depth-Anything-V2-Small, via Hugging Face Transformers
Trained on ~1.5M labeled plus ~62M pseudo-labeled images to predict relative depth from one frame — no stereo camera or LiDAR required.

## Slide 6: Where this stands
Working
Direction (left / right / center) reliably drives a full-size arrow on the OLED.
Just fixed
Distance was reading a per-frame renormalized preview image instead of the model's raw depth output — now uses raw values with self-calibrating near/far thresholds.
Next
Calibrate real near/far thresholds against the bottle's actual range; extend beyond a single object class.
github.com/himnshu-debug/TOLED-Display